## Slide 1: New Zealand Multibeam Experience
Kevin Mackay – NIWA
Andrew Price - LINZ

## Slide 2: History of the NZ multibeam experience
1996 responsibility for hydrographic services was transferred from the Royal New Zealand Navy to LINZ.
First NZ multibeam, HMNZS Resolution in 1998
  Atlas MD 2-30 100m-3000m range – damaged 2008 not repaired or replaced. Atlas Fansweep 20 MBES – removed December 2010
First civilian multibeam, RV Tangaroa in 2000
  Kongsberg EM300

## Slide 3: The first LINZ MBES standard
In 1998 LINZ published ‘HYSPEC’ the standards and specifications for conducting hydrographic surveys for LINZ, which was based on IHO publication S-44 IHO Standards for Hydrographic Surveys, Ed.3, and referenced a number of other industry publications of the time.
In 1999 LINZ collaborated with the Ocean Mapping Group to produce a multi-beam echo sounder (MBES) specification which LINZ merged with HYSPEC. The result was an internationally recognised publication for the acquisition and delivery of MBES data, which is still referenced by many hydrographic offices today.

## Slide 4: NIWA multibeams
Ikatere
  EM3002D
  EM2040
  GeoSwath Plus
Kaharoa
  EM3002D
Tangaroa
  EM302
  EM3002D
  EM2040

## Slide 5: Antarctic Surveys
  Ross Sea 2001, 2004, 2006, 2008
  Used LINZ MBES standard (incl. backscatter)

## Slide 6: LINZ HYSPEC v1.3
Notes: 1) Within NZ, LINZ HYSPEC has been reviewed and updated to bring it up to date with current best practice - still with a focus for acoustic sensors.
2) Went to consultation with trusted suppliers from industry in May 2015, feedback received in December 2015.
Key updates:
Alignment of SB orders with MBES orders for a single standard
Surveyor In Charge regional schemes e.g. AHSCP Level 1
Updated backscatter requirements - GEOHAB reference
Updated to completely digital deliverables to allow digestion straight into Bathy Database / Charting process
3) However; Still equipment driven - acoustic focus only.
Requirement for digital Standard Sheets retained.

## Slide 7
COLLECT ONCE - USE MANY TIMES
1. BATHYMETRY
2. BACKSCATTER
3. WATERCOLUMN
Notes: V1.3 is clear in its requirements for bathymetry but only touches on logging raw backscatter; no specification for processed backscatter or metrics and guidance around logging water-column. If that is to become a deliverable as part of a LINZ survey it will need specifying in order to QC it.

## Slide 8: Incorporating science data into nautical charts
Kermadec Volcanoes
~40 submarine volcanoes in NZ EEZ
Raoul
Macauley

## Slide 9: And the results…
NZ Risk Assessment - May 2016
Notes: In 2015 the NZHA undertook an evidenced based risk assessment of maritime traffic within New Zealand waters to identify areas of risk. The risk assessment was based on the novel methodology developed during the South-West Pacific Regional Hydrography Programme (SWPRHP) with the Ministry of Foreign Affairs & Trade (MFAT). The methodology uses a Geographic Information System (GIS) based risk model of 39 layers with a level of risk assigned to each cell within the layer. The cell resolution varied from ports & harbours, to the Territorial Sea limit, to the Exclusive Economic Zone (EEZ), with greater granularity in the ports & harbours where vessel movement becomes more critical. The layers included environmental, cultural and economic factors, as well as chart quality information and seabed characteristics.

## Slide 10
Notes: The outcomes of the risk assessment were analysed and areas of high to moderate risk were isolated for future survey work. The areas are expansive and our budget cannot cover them in their entirety. This opens the scope up to share work with other users interested in collecting Bathymetry, and gives us a long term view to help approach potential partners about collaborating.

## Slide 11: NZ Risk Assessment - May 2016
Areas of Heightened Risk Along Navigational Channel

## Slide 12: Project Concept
BUDGET
Notes: LINZ was primarily interested in collecting Safety of Navigation survey information in a buffer zone around the SOLAS traffic where the highest risk from the NZHRA is. MDC interested in Seabed Habitat Mapping & benthic terrain modelling. Both achieved from MBES.

## Slide 13: Requirements
Non-Acoustic Systems
Digital First, Data Centric
Marine Spatial Data Infrastructure
Joining Land & Sea
Technologically Agnostic + Outcome focused standards
Drivers
Notes: The hydrographic office is widening it’s scope; as we move towards MSDI, we are looking at fully quantative data across the littoral zone, merging datasets & datums. There is a requirement to utilise other sources of information; if we use them their uncertainties need to be understood and quantified. Currently the specification is purely acoustic but we need to broaden it’s scope. Keeping the standards technologically agnostic and outcome focused

## Slide 14: LINZ HYSPEC 2.0
IHO S-44 Review
LINZ HYSPEC v1.3 Review
Data Requirements & Technology Drivers
LINZ HYSPEC 2.0
Data Driven
Beyond Nautical Charting
Multi-source Multi-use
Notes: LINZ is reviewing all of our specifications; HYSPEC being one of them. Independent Review to digest in June. Assessment on implimentation and stakeholder engagement workshops - opened up to NZIS hydro stream.
The IHO has established a Hydrographic Surveys Scoping Project Team (H2SPT), which New Zealand (LINZ) was a member of, and we look forward to contributing to the international effort to update S-44
This work will inform the further development of a data driven LINZ specification to incorporate technologies such as LiDAR, SDB and CSD and other datasets required by broader range of stakeholders beyond the requirements for safety of navigation hydrographic surveys and e.g. the development and use of Maritime Spatial Data Infrastructure

## Slide 15: Questions?

## Slide 16: Multibeam Survey use in NZ
Public good science
Commercial
  sub-marine power and telecommunication cables
  marine mining
  offshore oil and gas projects
  site surveys for sewage outfalls, pipelines
Hydrographic
UNCLOS
  NZ and other States
Antarctic

## Slide 17: NZ region multibeam coverage
Surveyed ~25%
NIWA ~10%
Others ~15%
Notes: Still 4M km2 to survey, even surveying 365/24 would take 7 years but at our present rate more likely to take 40 years

## Slide 18: Multibeam – more than just bathymetry
2011 Water Column: Volcanic Plumes
Plume
Seafloor
Stack

## Slide 19
Bay of Islands Ocean Survey 20/20
40 days Tangaroa
35 days Pelorus
Multibeam – more than just bathymetry

## Slide 20: NIWA Multibeam protocols
Transit data
Data gap filling
Backscatter “calibration”
Water column data
Data storage
  Metadata
  Coverage polygons
  Processed data
  Raw data

## Slide 21: Existing Source Data - 1942

## Slide 22: Project Concept
BUDGET
Notes: The area covered by the RfP is identified in Figure 1. The area cross-hatched in red is the hydrographic survey area, to be surveyed to LINZ LINZ-1 standard which includes backscatter information for science purposes. The area between the area outlined in black and the area cross-hatched in red within QCS-Tory is to be surveyed to LINZ-2 standard. The combined area is approximately 43,300 hectares (ha).

## Slide 23: Joint Specifications - HS51
Notes: Very important to clearly demarcate requirements in geographic areas.
Fieldwork Year 1
Partial Deliverables Year 1
Full Deliverables Year 2

## Slide 24
LINZ MBES standards – John Hughes-Clark -> moved to Hyspec
Navy had guaranteed sea days for shipping lane work till Navy gave up hydrographic surveying
LINZ uses tender process for hydrographic work
All work focuses on bathymetry
No requirement for any backscatter
“Survey once, use many” a fallacy
“every ping is sacred” vs. bathy surface

## Slide 25: Queen Charlotte Sound - Northern Entrance 1st Iteration
Planned FY 15/16 - LINZ to provide Survey Specification & Data Validation
Notes: In the approach to Christmas 2015

## Slide 26: Surveys
Havre Volcano
http://earthobservatory.nasa.gov/IOTD/view.php?id=78849

## Slide 27: Surveys
Rumble III Volcano

## Slide 28: Surveys
2005 2010
0m
-100m
+60m

## Slide 29: Surveys
Bay of Islands
www.os2020.org.nz

## Slide 30: Surveys

## Slide 31: Surveys
Cook Strait
Hazard Identification
Faults
Landslides

## Slide 32: Surveys
West Coast Canyons