## Slide 1: Group Activity 1
AusSeabed.gov.au website discussion

## Slide 2: Introducing:
Action item from October 2016 workshop – develop website
  Share information
  Host outcomes of the working group
Registered .gov.au domain
  Marine.gov.au – too general
  Reflect aims of group
One-stop-shop
AusSeabed.gov.au
Notes: One of the action items from the October 2016 workshop was to develop a website
To share information
Serve as a host for other actions being undertaken by the group – survey register, coverage maps, tools, and anything else we need it to
The domain has been registered through the Domain Name Registrar held in the Digital Transformation Agency. Because it’s a .gov.au site we can’t just call it whatever we want to.
Marine.gov.au is considered far too general for this program and though it hasn’t been claimed yet, there are other agencies that have a stronger claim to use “marine”
The name needed to be something that closely reflects the aims of the group – but also doesn’t hold us back from expanding – so multibeam was a bit too specific.
AusSeabed was settled on as a balance between a whole-of-Australia initiative and covering the current focus on multibeam but also allowing us to include many other data types later on
This website will be the one-stop-shop for updates on the activities on the working group and provide access to the tools and products we create

## Slide 3: Other information
Timelines
  Domain registered October 2017
  Sitemap and content agreed by partners – end of year
  Live site – 1st qtr. 2018
Structure and functionality – fundamental
Notes: In terms of timelines,
The domain was registered last month
Once we have an agreed sitemap to give to the developers they can have a basic beta site up in under 6 weeks
We’re aiming for it to be fully live and functional in the first quarter of next year – likely before then but getting the right approvals and clearance on content and functionality takes time and is something that we can’t avoid – that takes time.
But before we start getting developers too involved, we need to make sure the structure of the site is one that everyone will find useful and serve our needs.
That’s where you all come in – we need your feedback on the draft structure and general functionality.
Walk through the structure and then split into groups to go through it in more detail.

## Slide 4
Notes: Step through sections
There’s 2 stages to the website to think about
The product functionality will be quite basic to begin with – there is no portal right now
Likely a shapefile that we send out, and gets emailed back, we update the website from GA
In the future we’d like to see something far more interactive and self-contained on the website
But the information that as users we need from the coverage compilation, survey register – that will be the same, no matter what the functionality is on the website
Data is an area we will cover later in the day, during activity 3 so leave this discussion for now.

## Slide 5: AusSeabed.gov.au
What do you want to see on the AusSeabed.gov.au website? Is it already accounted for?
Are there existing sites (national/international) that already have useful information we can draw on?
Logos and parties that will be represented on the ‘Partners’ page.

## Slide 6: Group Activity 2
National tools

## Slide 7: Outcomes of activity:
Identify and prioritise utilities, tools, methods that could be used or adapted to facilitate our national initiative.
A table is provided to guide the discussion and outcome.

## Slide 8: Group Activity 3
Data submission and accessibility

## Slide 9: Data submission and accessibility
What portals are out there we can use as role models to submit and access data?
How do you want to submit and access data?
What tools and formats do you prefer using?
What volume of data would you submit after a typical survey? (All data types including bathy, backscatter, and water column)
How often do you want to access data?
Should we include embargoed data and under which conditions? For example, limiting the embargo timeframe.
For open access data, are there any licensing issues that need to be considered?

## Slide 10: Group Activity 4
Survey register and data coverage discussion

## Slide 12: Survey register and data coverage discussion
Survey Register
What information do you want to see on the planned survey register?
What is the minimum metadata that should be required? Mark these fields as ‘mandatory’.
Are there existing sites (national and international) that already have useful tools that we can draw on?
What would help you use the survey register – to register surveys, access the information, and complete other reporting requirements?
Data coverage
What metadata should be associated with coverage submission? (In addition to fields in the survey register, think of point density, grid resolution, etc.)
What data should be included in the coverage? Open access, embargoed, etc.
What method should be used to derive the coverage? e.g. polygons derived from gridded data, from point data or just tracklines?
Should we produce a guideline to show how to create coverage files and submit them? For example, for a polygon derived from gridded material, should we specify the resolution it is derived from?

## Slide 13: Group Activity 5
Ironing out the national multibeam guideline

## Slide 14: Where does it fit amongst the many existing ones?
IHO, MSQ, NOAA, MBARI, UNH, LINZ, MESH, NESP, etc
National Guideline
Common minimum requirements to ANY surveys
To facilitate National accessibility and interoperability
NESP
Specifications for mapping marine reserve (baseline or monitoring)
Charting
Specifications to map for charting
Infrastructures
Specifications to build or monitor infrastructures
IHO
LINZ
NOAA
MESH
MSQ
NOAA Integrated Ocean and Coastal Mapping, 2011
(Multi-purpose)
German guideline
Woodside
BP
Total
Shell
etc
CHS
NOAA-IOCM
Example of specifications for various purposes

## Slide 15: How is this guideline different from others?
Includes material and links specific and relevant to Australia seabed mapping needs
Addresses requirements that should be a minimum to ANY seabed mapping survey.
Other guidelines or standards are purpose-specific and should build on this National guideline
This guideline is a product of the whole working group

## Slide 16: Activity Part 1 – Agreement on specifications
Specification | National Guideline Australia | NOAA IOCM Seafloor Mapping Guidelines (Oct 2011). Based on IHO order 1 | IHO Order 1
Purpose | Overall minimum requirements to insure minimum standards and facilitate data submission and accessibility | For the data to be used confidently by any NOAA program, Will allow products derived from surveys to be used for either nautical chart or fish-habitat mapping purposes | Charting for areas shallower than 100 metres where under-keel clearance is less critical but features of concern to surface shipping may exist or is not an issue
Survey planning | Survey register and available data Authorities |  | 
Sonar frequency |  | Depth Range (m) *Frequency (f; kHz) 5–100 240<f≤–450 50–200 180<f≤240 200–1000 50<f≤180 1000–3000 12<f≤50 3000–12000 f ≤12 | 
Data type | Bathy: Mandated Seabed Backscatter: Mandated Water column backscatter: Recommended | Bathy: Mandated Seabed Backscatter: Mandated Water column backscatter: N.A | Bathy: Mandated Seabed Backscatter: N.A Water column backscatter: N.A
Mapping coverage | 2 basic types of surveys: 100% coverage (10% overlap of the “good” swath) Partial | Full coverage with 5% overlap. Reconnaissance-style mapping may be necessary due to time constraints. | 
Resolution | 2 m resolution in 5 m to 40 m depths; 5% of depth beyond 40 m (LINZ-1) | 2 m resolution in 5 m to 40 m depths; 5% of depth beyond 40 m | 2 m resolution in 5 m to 40 m depths; 5% of depth beyond 40 m
Depth reference |  | Depth is measured from the sensor face. For sonars deployed from submersibles, the estimated depth of the transducer face depends on the delay from the last GPS-estimated position and account should be made for inertia-sensor drift. | 
Depth uncertainty | a = 0.5 m, b = 0.013 (IHO order 1) or a = 1.0 m, b = 0.023 (IHO order 2) OR LINZ-2 (IHO order 1) Or LINZ 3 ( a = 0.625 m, b = 0.0185) | 95% probability level, after corrections for systematic error, e.g., water level, = ±√[a2+(b*d)2], where a = 0.5 m, b = 0.013, and d is the depth (= 0.5 m at 5 m depth, and = 2.6 m at 200 m depth) | 95% probability level, after corrections for systematic error, e.g., water level, = ±√[a2+(b*d)2], where a = 0.5 m, b = 0.013, and d is the depth (= 0.5 m at 5 m depth, and = 2.6 m at 200 m depth)
Vertical Reference | GDA2020 or ITRF with epoch reference | Appropriate Chart Datum (e.g., Mean Lower Low Water or Low Water Datum in non-tidal areas), or WGS 84 ellipsoid, | 
Tides | Record GPS tide Min 1 Tide gauge desirable to enable conversion to terrestrial datum If while mapping, requires to refer to MSL, coordinate, in advance of surveys, with the Bureau of Meteorology (BOM) to prepare predicted tides | Should consider tide predictions, water level observations, datum references and zone corrections. The practical minimum for water level error is 0.20 m and allowable maximum is 0.45 m at the 95% confidence level. Platforms with inertial motion unit (IMU) systems should record the raw data input to the IMU. Coordinate, in advance of surveys, with the National Ocean Service’s (NOS) Center to prepare tidal zoning charts. may require the installation of water level gauges or, in areas where water level gauges or shore-based kinematic GPS are not available, installation of specialized GPS equipment on the survey vessel and subscription to specialized globally-corrected GPS (GcGPS) services. | 
Sound speed Profiles (SVP) of uncertainty due to refraction. For beam-steering sonars, measurements of sound speed should be made continuously at the location of the sonar transducer. | Min of 1/day, but should be monitored. If sound speed at the transducer varies by > 2m/s another SVP should be collected | SVP are needed Frequency depends upon the type of mapping project and the time spent in a location. (frequent, e.g., 2 hr or less, in areas of increased water column variability) In transit collected at least twice a day in open-ocean and more frequently (e.g., 4-6 casts per day) in continental-shelf areas. To estimate SVP from XBT data, the depth-averaged mean salinity from a nearby CTD cast should be used not the salinity measured at the sea surface. For transits SVP, a few casts may not provide accurate raytracing solutions; these may be used, however, to bracket the estimates | 
Horizontal Reference | GDA2020 or ITRF with epoch reference | Positions referenced to WGS 84 (NAD 83) | Positions referenced to WGS 84 (NAD 83)
Horizontal uncertainty | 5m +5% of depth (IHO order 1) or 20m +10% of depth (IHO order 2) | 95% probability level, after corrections for systematic error, e.g., water level, =5 m + 5% of depth (5.25 m at 5 m depth = 0.003 latitude min, 15 m at 200 m = 0.008 latitude min.) | 5 metres + 5% of depth
Seabed Backscatter | Always collect during survey and collect minimum calibration line during Patch test (Appendix G) | Collect over the full-depth range. This is dependent on the sonar system’s capability. If constrained by data storage capacity, reduce the sampling rate or store only average beam intensities. | 
Water Column Backscatter | Collect Data download to Repository |  | 
Classification ground truth | Follow NESP seabed sampling guideline. Should be done with backscatter calibration in mind Should be done for the shelf, not required in depth > 200m | Optical or grab samples sufficient in quality and quantity to ground truth areas of backscatter differentiation, and not to exceed a lateral spacing of 2000 m. Unless required by the primary mission, optical or physical sampling of the seafloor is not required in depths exceeding 100 m. | 
Metadata | Data owner, Survey area, Date, Vessel name, Operator (s), Geodetic parameters, Line plan, Equipment list, Level of standards expected or achieved Additional data (samples, videos, etc) Sound velocity profile being used and refraction applied, Tidal data used (if any) MBES Data types and explanation why not collecting a type | Minimum FGDC compliant; ISO 19115 preferred | conform to the “IHO S-100 Discovery Metadata Standard Minimum: - the survey in general e.g. purpose, date, area, equipment used, name of survey platform; - the geodetic reference system used, i.e. horizontal and vertical datum including ties to a geodetic reference frame based on ITRS (e.g. WGS84) if a local datum is used; - calibration procedures and results; - sound speed correction method; - tidal datum and reduction; - uncertainties achieved and the respective confidence levels; - any special or exceptional circumstances; - rules and mechanisms employed for data thinning.
Point data attribution | All data should be attributed with its uncertainty estimate at the 95% confidence level for both position and, if relevant, depth. |  | All data should be attributed with its uncertainty estimate at the 95% confidence level for both position and, if relevant, depth.
Archiving | National Data Centre | Raw and processed geophysical data, with metadata, should be submitted to National Geophysical Data Center (NGDC) within 1 year of acquisition. Additional oceanographic data should be delivered to the National Oceanographic Data Center (NODC) also within 1 year of collection. Raw data is in the form generated by the sensor, without corrections applied. | 

## Slide 17: Ideas to consider – Part 1 Standard
Are we expecting too much from any seabed mapping?
Are these specifications realistic?
Will you follow them or is it “for others”?
Is our guideline meeting an IHO/LINZ/other standard already?
If so, should we refer explicitly to it and highlight additional expectations (see comparison table). What are the Pros and Cons of doing so? Are we making it too difficult for the general seabed mapper?

## Slide 18: Part 2 – Guideline review
1 Introduction
1.1 Scope
1.2 Related Standards and Publications
Glossary
2 Pre-Survey Planning
2.1 Survey register and National coverage
2.2 Liaison with Local Authorities
2.3 Seabed mapping objectives
2.4 Project instructions
2.5 Field Survey Instructions
2.6 Seabed samples
2.7 Submission of Data
3 Mobilisation and Calibration
3.1 Systematic Errors
3.2 Mobilisation
3.3 Horizontal Positioning
3.5 Vertical positioning
3.6 Tidal Station
3.7 Patch Test
3.8 Seabed Backscatter Calibration
3.9 Water Column Backscatter Calibration
3.10 Built-in Systems test
3.11 Final acceptance test

## Slide 19
4 Acquisition
4.1 Survey Plan
4.2 Seabed and Water Column Backscatter
4.3 Ancillary Systems
4.4 Raw datasets
4.5 Monitoring and QA/QC
5 Reports
5.1 Pre-planning Report or Survey Register
5.2 Calibration Report and Records
5.3 Report and Records of survey
6 Standards
7 Processing and Rendering of Data
7.1 Data Processing
7.2 Data Rendering
8 Appendices
Appendix A – Survey register metadata
Appendix B – List of Authorities
Appendix C – Guideline on Timelines for Actions
Appendix D – Horizontal positioning
Appendix E – Tide gauge calibration
Appendix F – Total Propagated Uncertainties
Appendix G – Patch Test method
9 References

## Slide 20: Part 2 – Guideline review
When reviewing each section, think of:
Is the heading and sub-heading appropriate?
Is this the appropriate section to be in?
Should this be merged with another section?
What is the minimum material that should be included in the guideline for each section?
Is the material included too similar to another SOP – would it be simpler to refer to another SOP for particular sections?
Would you follow this recommendation or is it “only for others”?
What appendices should we include?
What should be in the glossary?
Are we addressing end user needs?
Can end-users understand what will come out following this guideline (purpose, resolution, etc)?
Should we have an end-user friendly section explaining how to use the guideline and what sections are particularly relevant to them?
How should we deal with authorship?

## Slide 21
2 groups of end users
Non-experts
  Managers
  Researchers
Experienced
  Surveyors
  Field experience
2 survey purposes
Charting
Science

## Slide 22: Part 3 – Remaining sticking points

## Slide 23: Where to next? Guideline
Timeframe for guideline
Who:
  Complete section, incl. appendices
  Review the whole document
  Format the document
Release method
  Where
  Promotion/communication products
Industry/other commercial players: how do we progress uptake?
Next version
Complete Sections
08/12/17
Release v.1
01/04/18
Formatting
15/02/18
Section Review
01/02/18
Overall review
07/03/18

## Slide 24: Where to next? Other
Future meetings
  AGU 2017
  Geohab 2018
  AMSA 2018
  Hydro 2018
  Products
  AHS
  Interntional Hydro paper
  Data management (AHO-GA discussion)