## Slide 1
Deriving an Intertidal DEM from GA’s Intertidal Extents Model (ITEM)
Stephen Sagar
National Earth and Marine Observations Branch

## Slide 2: The Intertidal Extent Model (ITEM)
Objective: To model the extent and topography of the intertidal flats of Australia’s coastline utilising 28 years of the Landsat archive

## Slide 3: How and why do we want to map the intertidal zone?
Remote sensing is a cost effective option, but still subject to tidal regimes and environmental factors. Recent single image analysis (Dhanjal-Adams et al., 2016) has estimated Australia’s tidal flats at a minimum area of 9,855km2
An important coastal ecosystem, characterised by high productivity and biodiversity and providing habitat for migratory shorebirds worldwide
Provides critical coastal protection from extreme storm events, and is often a component of the coastal geomorphologic system around high value commercial asset sites such as ports.
Capturing information on the extent and topography of the intertidal zone, particularly at a continental scale, is a challenging and costly exercise.
The physical environment makes traditional surveying methods difficult to implement, and acquisition of airborne elevation data (LiDAR etc) is expensive and subject to tidal regimes of the study site.

## Slide 4: Digital Earth Australia (DEA)
ITEM v1 on the Australian Geoscience Data Cube (AGDC) prototype
221 Coastal 1° by 1° coastal cells
Over 200,000 tiled observations
Average of 859 observations over 28 yrs
A continental archive of 28 years of analysis ready Earth Observation data
Processed to nadir view angle, BRDF, atmospherically corrected surface reflectance (NBAR)
Pixel Quality flags for cloud, cloud shadow, saturation
Notes: Geoscience Australia in collaboration with the CSIRO and Australia’s National Computation Infrastructure have fundamentally changed this paradigm by taking a new approach that involves:
  Moving all available satellite data onto high-speed storage that is co-located with high-performance computing (i.e. fast disks connected directly into one of the Southern Hemisphere’s fastest supercomputers)
Calibrating and correcting all of the data so it is already prepared for subsequent analysis, i.e. we’ve taken account of the fact that each observation is from a different
  time of day
  season of the year
  angle of observation
  In effect we’ve lined up every observation and removed anything that might stop us from directly comparing one observation with the next. We’ve even accounted for the fact that over the last 30 years, Australia has moved over a metre to the northeast so that we’re confident that you can drill straight through the data and see how the landscape has changed
This has produced an enormous reduction in the time required to produce a new information product. By calibrating the entire data stream to the same standard and making the data accessible in a High Performance Data (HPD) structure co-located with a High Performance Computing (HPC) facility, the data can be viewed as enabling infrastructure for data- intensive science.
The Digital Earth Australia Program will deliver robust data infrastructure, standardised services and information products that will:
1. Increase the efficiency and effectiveness of Australian government programs and policies that need accurate and timely spatial information on the health and productivity of Australia’s landscape.
2. Enable Australian business to quickly capitalise on open data, and create new capabilities to increase efficiency, productivity and employment opportunities.

## Slide 6: Continental Scale Tidal Modelling
Oregon State Tidal Prediction Software (OTPS)
(Egbert and Erofeeva, 2002)
A tidal harmonics based regionally validated model with <5cm RMSE misfit
Our testing against the Hydrographic Office Austides record show a RMSE misfit of ~10-15cm
We use the OTPS TPX08 model, consisting of a multi-resolution bathymetric grid solution, with a 1/6° solution in the global open ocean, and a 1/30° local resolution solution to improve modelling in complex shallow water environments.

## Slide 7: The Observed Tidal Range (OTR)
A sun-synchronous sensor – observes at the around the same time of the day for each observation
This means that even with tidal variations, we most likely will only observe a portion of the full tidal range
We can characterise this as highest (HOT) and lowest (LOT) observed tide

## Slide 8: The Intertidal Extents Model (ITEM) Process
Lowest Observed Tide (LOT)
Highest Observed Tide (HOT)
Each tile stack of observations is attributed with a tidal height utilising the OTPS model
Observations are the reordered based on tidal height rather than time
The Observed Tidal Range is divided into 10 equal interval buckets to create ensemble stacks of observations for each 10% of the range

## Slide 9: The Intertidal Extents Model (ITEM) Process

## Slide 10: The Relative Extents Model
Models the Extent and Topography of the Intertidal Flats
Layers values reflect the spatial extent of the exposed intertidal land surfaces at intervals of the OTR
Modelled up to the highest 80% of the OTR
Roebuck Bay, Western Australia

## Slide 11: ITEM Model Examples
Talbot Bay, The Kimberley, Western Australia

## Slide 12: Deriving a Digital Elevation Model
Tidal height attribution to each individual observation enable us to evaluate the distribution of the heights within each interval
Each distribution corresponds to the extents of the interval in the Relative Extents model
Median heights are used to attribute waterline contours at the boundaries of the intervals extents.
The uncertainty of the extent area is reflected in the standard deviation of the heights used to model the interval.

## Slide 13: Model Validation - Darwin, Northern Territory

## Slide 14: Model Validation - Moreton Bay, Queensland
Mean Absolute Height Residual = 0.15m

## Slide 15: Integrating the Intertidal DEM in the Northern Australian 100m Bathymetry Grid
Work completed by Dr Robin Beaman (JCU) and Geoscience Australia
ITEM is effective in these sometimes highly turbid areas where water column Satellite Derived Bathymetry methods are restricted.
Tidal ranges of over 6m, and intertidal flats 10’s of km wide

## Slide 16: Integrating the Intertidal DEM in the Northern Australian 100m Bathymetry Grid
The ITEM DEM is effective is delineating very shallow reef features, shoals and platform features that can be missed in coarser resolution and deeper water surveys.
Acts as a complementary data source to produce a more realistic land/sea interface in the grid

## Slide 17: Integrating the Intertidal DEM in the Central QLD and GBR 30m Bathymetry Grid
Produced in collaboration with Robin Beaman (JCU) for the QLD Environment and Heritage Sub and Intertidal Mapping Project

## Slide 18: ITEM v2 – What can we improve?......
Tidal Modelling in ITEM v1 was constrained by the cell boundaries of the AGDC.
Whilst errors were reflected in the Confidence Layer values, the DEA offers us a more flexible approach.
Adaptive partitioning provides a multi-resolution polygon framework for tidal modelling.
Regions with higher spatial variation in tidal range can be represented by a denser partition structure and tailor to coastal features

## Slide 19: A New Tidal Modelling Framework
ITEM v1 - AGDC
ITEM v2 - DEA
New Model extends to cover more offshore reefs and the GBR
Will underpin historical coastal remote sensing product generation on DEA

## Slide 20: Improved modelling and more complete archive in DEA
The Tiwi Islands, Northern Territory
ITEM v1
ITEM v2

## Slide 21: Using composite imagery to explore change dynamics
Burnett River Mouth, QLD
Imagery can be constrained to specific tidal ranges over time to reduce tidal influence
Specific temporal ranges can be examined to isolated changes based on events such as flooding and cyclones

## Slide 22: Where to next?
Focus on exploring the coastal stability potential of the model
More extensive validation through field work
Development of an operational DEM workflow and localised modelling for complex coastline and estuarine environments
What ITEM is not designed for….
Modelling the profile or elevation of areas that aren’t inundated in the tidal cycle (ie. beach profiling)
Of limited use in micro tidal regions with a steep sloping shoreline or breaking waves
Cannot model obstructed intertidal regions, ie vegetation cover, mangroves

## Slide 23
Contact: Stephen Sagar
stephen.sagar@ga.gov.au
Project Team:
Stephen Sagar
Biswajit Bala
Dale Roberts
Leo Lymburner
Claire Phillips
Data Access:
http://dap.nci.org.au/thredds/catalog.html - GA Earth Observations - Derived
or
http://eos.ga.gov.au