## Slide 1: Survey Linear Distance Estimation
General overview of process to generate survey line mile calculations for planning purposes
Dr. Elizabeth Johnstone, IXBLUE AUSTRALIA
David Donohue, Director of IXBLUE AUSTRALIA
8 November 2017

## Slide 2: Survey Line mile calculation - complex
HydroScheme HI – Sahul Banks
>360,000km2 - How many survey line miles to survey to IHO Order 1a (or better)???

## Slide 3: Traditional method
Break it up into Data Acquisition Blocks
Further segment DAB into common depth zones
COTS Line planning tool(s) to calculate line miles per depth zone

## Slide 4: Traditional method
187km
339km
372km
179km
767km
Total: 1,847km

## Slide 5
Line Planning for Area N2

## Slide 6
Line Spacing for Area N2
Red 90m
Gold 180-270m
Green 330m
Cyan 800m
Teal 1300m
Blue 1665m
180m
330m
90m
210m
270m
330m
1665m
800m
90m

## Slide 7: Answer: 213,105nm
Excluding transit time, end of line turns, cross lines, seafloor sampling.
4 weeks effort (145 DAB)
Fixed parameters
Better way?

## Slide 8: Aim/Brief:
Develop software work flow to rapidly assess linear distance required to survey a large area
Generate an Apriori linear nm assessment using an area based approach
Using open source ‘free’ software if possible

## Slide 9: Solution:
Open source GIS known as SAGA
(System for Automated Geoscientific Analysis)
  - Predominantly used, full featured, free for commercial use
Quantum GIS (QGIS)
  - used to convert S-57 soundings to raster format for combination with GEBCO
  - open source & free for commercial use

## Slide 10: Workflow overview
1. Convert all vector sources (if any) to uniform raster grids with depth encoding, with quantifiable cell edge lengths (ie (10m, 10m) on a UTM projection, or (926m x cos(Ø), 926m) for a 30 arc second geographic grid
2. Load gridded raster bathymetry data

## Slide 11: Workflow overview
3. Conduct a calculation on each grid cell that determines the optimal line spacing & total distance to cover that grid cell, using cell edge length & mean depth within the cell.
Store the calculated results in a new grid.

## Slide 12: Workflow overview
4. Create a polygon encapsulating the survey area of interest.
5. Generate a sum of all linear nm grid cells bounded by the polygon.

## Slide 13: Example:
Reclassified raster with grid cells based on mean depth (GEBCO + ENC) and clipped to Australia/Antarctica/Outer Islands EEZ boundaries

## Slide 14: Line Mile Parameters for Calculations* (EEZ Example)
Depth Range (m) | Swath Multiple | Coverage (%) | System
2-5 | 6 | 200 | Dual head
5-15 | 6 | 200 | Dual head
15-50 | 4 | 130 | 200-400kHz
50-100 | 4 | 130 | 200-400kHz
100-200 | 4 | 120 | 90-150kHz
200-500 | 4 | 110 | 
500-1000 | 4 | 110 | 
1000+ | 4 | 110 | 30kHz
* All parameters are adjustable for the survey line mile calculations. Output is delimited by depth bands within each shapefile.

## Slide 15
Survey Line Miles
comparing shallow vs deep

## Slide 16: Further Considerations/Caveats
Tidal Variation & Datum
GEBCO uses WGS84 MSL vertical datum model (defined on EGM96 equipotential model)
NOT the WGS84 ellipsoid ‘zero’
GEBCO dataset will not give the ‘worst’ performance estimate of swath width. Instead, it will give a result near to the long term average performance of swath width
Areas characterised by shallow waters and large tidal ranges will have more ‘uncertainty’ than deeper areas