## Slide 1
International Multibeam Backscatter Working Group (BSWG) – update
Overview of the BSWG
Highlights from BSWG Report and the special edition of Marine Geophysical Research:
  Calibration
  Acquisition
  Processing
Future activities

## Slide 2: Overview of the BSWG
BSWG created in 2013 as part of a QPS backscatter workshop ran as part of the Geological and Biological Habitats conference series. Website:
  http://geohab.org/BSWG/
“…standardisation of the acquisition and processing of sonar backscatter data provided by multibeam echosounders”
BSWG Report published in 2015 Le Marche and Lurton (2015):
http://geohab.org/wp‐content/uploads/2014/05/BSWGREPORT‐MAY2015.pdf

## Slide 3: Backscatter calibration
From Lamache and Lurton (2017), there are two types of backscatter data calibrations:
Absolute calibration, enabling the sonar to measure true referenced physical values of backscatter, and
Relative calibration, ensuring self-consistency of the measurements by one system, without an absolute reference of the backscatter level.

## Slide 4: Backscatter acquisition
Backscatter settings, from La Mache and Lurton (2017):
Optimal backscatter data acquisition requires specific settings that may differ from those required for optimal bathymetry data acquisition.
Acquisition settings should be kept as stable as possible, rather than using the varying, automated modes incorporated in many MBES today
Source level vs power setting (Taken from Welton, 2014)

## Slide 5: Backscatter acquisition
Sketch of swath overlap where specular reflection and outer incidence angles (high and low angles—shaded) are covered by intermediate ‘stable’ incidence angles (From: La Mache and Lurton, 2017)
Insonification angles between about 20° and 60° offer the best quality of data
Acquisition conditions should be as similar as possible for repeat surveys (e.g., heading directions, survey line patterns, and sonar settings), in order to minimize the artificial variations

## Slide 6: Backscatter Processing
Most software follow a similar processing chain
Subtle differences in how different steps are implemented, e.g:
  Beam pattern correction
  Insonification area
  Angular correction
The backscatter data processing chain (From: Schimel et al, in review)

## Slide 7: Future activities
Comparison of software - Alex Schimel
Calibration protocols
Water Column group
Repeatability of backscatter measurements
???