## Slide 1: Program 2 - Rapid Spatial Analytics
Bathymetry Coordination
Cost Effective Seabed Mapping
Dr Nathan Quadros, General Manager

## Slide 2: Coastal & Urban DEM Project
COAG initiative with then Department of Climate Change
Performance of DEM technologies in coastal environments
Integration of multi-resolution DEMs
Vertical datum transformations in the littoral zone
Hydrological conditioning of DEMs
User requirements and technologies for bathymetric data collection
User Driven acquisition and product specifications
LiDAR Compliance and Quality Assurance
Data and flood visualisation

## Slide 3: Coastal & Urban DEM Project

## Slide 4: Bathymetry User Needs
Note: 110 responses from 234 contacts
Chart: 
| Federal Government | State Government | Local Government | Port Authorities | Private Companies | Academia | Coastal Boards and Committees | New Zealand
Response | 20 | 31 | 8 | 7 | 14 | 11 | 2 | 15
No Response | 24 | 30 | 14 | 14 | 5 | 20 | 14 | 3

## Slide 5: Bathymetry User Needs
Chart: 
| Law Enforcement and Defence | Marine Construction and Infrastructure | Mineral Resources | Commerical Fishing and Aquaculture | Marine and Coastal Tourism | Coastal Zone Management | Marine and Coastal Conservation | Natural Disaster and Hazard Mitigation | Pollution and Environmental Protection | Identifying Wrecks and Dives | Boundary Delimitation | Maritime Navigation | Hydrographic Charting | Data Collection and Acquisition | Spatial Data Custodian and Sales | Climate Change and Flood Modelling | Storm Surge Modelling and Impact | Tsunami and Tidal Wave Modelling | Hydrodynamic Modelling | Ecosystem Modelling | Marine Habitat Mapping | Seafloor Mapping | Other
 | 13 | 34 | 20 | 14 | 8 | 55 | 41 | 35 | 26 | 21 | 34 | 25 | 37 | 72 | 26 | 37 | 37 | 25 | 34 | 31 | 51 | 51 | 14

## Slide 6: Bathymetry User Needs
Chart: Percentageof Respondents Showing Interest
| Shipping and Boating Channels | Sea Grasses | Platforms and Infrastructure | Reefs | Marine Habitats | Ports and Harbours | Shoals | Man-Made Seafloor Features | Wrecks
Coastal Modellers | 0.36111 | 0.47222 | 0.38889 | 0.69444 | 0.58333 | 0.41667 | 0.66667 | 0.36111 | 0.38889
Maritime Operations | 0.9 | 0.25 | 0.55 | 0.5 | 0.3 | 0.85 | 0.75 | 0.7 | 0.7
Overall | 0.42056 | 0.40187 | 0.34579 | 0.63551 | 0.51402 | 0.45794 | 0.58879 | 0.3271 | 0.42056

## Slide 7: Bathymetric LiDAR

## Slide 8: Bathymetric LiDAR
 | Fugro LADS Mk3 | Optech SHOALS 3000 | Optech SHOALS 1000T | Optech CZMIL | Optech ALTM Aquarius | AHAB HawkEye IIB | AHAB Chiroptera | Riegl VQ-820-G
Typical Sensor Environment | Bathy | Bathy | Bathy | Topo-Bathy | Topo-Bathy | Bathy | Topo-Bathy | Topo-Bathy
Origin | Australia | Canada | Canada | Canada | Canada | Sweden | Sweden | Austria
Year Released | 2011 | 2010 | 2005 | 2011 | 2011 | 2009 | 2012 | 2011
Laser Wavelength/s | Green 532nm | Green 532nm Infra-Red 1064nm | Green 532nm Infra-Red 1064nm | Green 532nm Infra-Red 1064nm | Green 532nm | Green 532nm Infra-Red 1064nm | Green 532nm Infra-Red 1064nm | Green 532nm
Laser Energy Per Pulse | 7mJ@532 | 4mJ@532 | 4mJ@532 | 3mJ@532 | 0.1mJ@532 | 3mJ@532 | 0.1 mJ@532 | 0.02mJ@532
Measurement Frequency | 1.5kHz@532 | 3kHz@532 | 1kHz@532 | 10kHz@532 70kHz@1064 | 33-70kHz@532 | 4kHz@532 128kHz @1064 | 36kHz@532 400kHz @1064 | 200kHz@532
Nominal Laser Footprint @ Water Surface | 3m@532 | 2m@532 | 2m@532 | 2m@532 | 0.3-0.6m@532 | 4.m@532 0.5m@1064 | 1.5m@532 0.2m@1064 | 0.6m@532

## Slide 9: Bathymetric LiDAR
 | Fugro LADS Mk3 | Optech SHOALS 3000 | Optech SHOALS 1000T | Optech CZMIL | Optech ALTM Aquarius | AHAB HawkEye IIB | AHAB Chiroptera | Riegl VQ-820-G
Typical Sensor Environment | Bathy | Bathy | Bathy | Topo-Bathy | Topo-Bathy | Bathy | Topo-Bathy | Topo-Bathy
Nominal Flying Height | 400-700m AGL | 300-400m AGL | 300-400m AGL | Nominal 400m AGL | 300-600m AGL | 250-500m AGL | 250-600m AGL | Nominal 600m AGL
Swath Width (as a function of point spacing or altitude) | 585m@8x5m 360m@5x5m 125m@2.5x2.5 | 160m @2x2m 300m @3x3m | 60m@2x2m 130m@3x3m | 291m | up to 0.93 x AGL | 160m-260m @400m AGL 100m @250m AGL | 300m @400m AGL | 400m
Typical Point Spacings | 2x2m -8x5m | 2x2m - 5x5m | 2x2m - 5x5m | 2x2m | 0.4x0.4m - 1x1m | 0.5x0.5m - 3.5x3.5m | 0.4x0.4m - 1 x 1m | 0.2x0.2m - 0.8x0.8m
Minimum Water Depth | ~0.5m | ~0.3 m | ~0.3 m | ~0.1 m | ~0.1 m | ~0.5 m | ~0.1 m | ~0.1 m
Typical Maximum Water Depth | ~60m 2.5-3 x Secchi depth | ~50m 2-2.5 x Secchi depth | ~50m 2-2.5 x Secchi depth | ~50m 2.5-3 x Secchi depth | ~20m 1 x Secchi depth | ~40m 2-3 x Secchi depth | ~20m 1 x Secchi depth | ~15m 1 x Secchi depth
Commercial Opportunities in South-East Asia, Australia and the Pacific | Fugro LADS | No Commercial Operations | SHOALS 1000T was used in Northern Australia by Fugro Pelagos | None Currently | ALTM Gemini operator - AAM Pty Ltd | AAM Pty Ltd - Pelydryn operated. | None Currently | Fugro LADS

## Slide 10: Bathymetric LiDAR

## Slide 11: Satellite Derived Bathymetry
Heron Island, WorldView-2 by EOMAP

## Slide 12: Vertical Datums

## Slide 13: Western Port DEM

## Slide 14: Victorian Coastal DEM
Partnership with DELWP. Data supplied by Deakin University, Port of Melbourne and AHS was combined with existing DEM datasets including the 2010 VCDEM, the 2014 Western Port DEM and National Elevation Data from Geoscience Australia
Successfully added close to 1,800 km2 of high resolution bathymetric data to the 2010 VCDEM

## Slide 15: Victorian Coastal DEM
Updated High Res DEM
Continuous DEM

## Slide 16: Complimentary Technologies
Satellite Imagery Derived Bathymetry
Bathymetric LiDAR
Multi-Beam Vessel
WorldView derived bathymetry out to its depth extinction ~20m
If satellite derived bathymetry is successful, bathymetric LiDAR cross-strips and along coast flights to calibrate and validate
Bathymetric LiDAR coverage of major townships, and significant environmental areas
Multi-beam vessel coverage in critical areas with no coverage