## Slide 1: MBES Performance Testing The AI-MAC Approach
Multibeam Echosounder Working Group
Geoscience Australia
November 8, 2017
Nicole Bergersen
Acoustic Imaging Pty Ltd

## Slide 2: AI – Structure & Operational Philosophy
Primarily a technical knowledge centre
20-year Australian owned and operated private company
Provide subject matter expertise to MBES users, manufacturers of hardware, software and MBES survey stakeholders.
Deliver hardware, software, teaching and consulting services with a survey-outcome focus
Track record of introducing innovative techniques to the maritime industry in Australia and internationally.
Notes: I don’t intend for this to be a commercial talk ….
but
unfortunately this a commercial service
as well as good policy
So that is Acoustic Imaging….

## Slide 3: Genesis of AI-MAC Service
AI has a keen interest in understanding systems, the data they produce, and what the data tell us in terms of real-world performance and functionality of systems.
Highly proficient and experienced in system mobilisations, calibrations, validations, and near shore / shallow water working environments. In Australia AI has developed methods and approaches that are implemented across Australian private and government MBES users and ensure a higher quality of data is collected.
N Bergersen (AI) provided shallow water and vessel of opportunity (VOO) approach as Acoustic Imaging’s contribution to our industry partnership with the UNH Centre for Ocean Mapping (CCOM) program to converge with deep water approach provided by P Johnson of the US Multibeam Advisory Committee (MAC).
A combined approach was developed between AI and MAC through 2015-16, and is currently being applied to small and large vessel, deep and shallow water in the US and Australia.
Latest efforts focused on increasing manufacturer independence across all VOO.

## Slide 4: AI-MAC Core
Nicole Bergersen
  Lead Scientist Acoustic Imaging. Co-Director of AI-MAC. Systems integration, numerical and statistical approaches to system performance. Particilar application to shallow water VOO.
Lindsay Gee
  Ocean Science Director E/V Nautilus Research vessel. Deep water background. Current research efforts Backscatter + Mid-water column seep and feature mapping. NOAA MBES Advisory Group, IHO committee member.
Douglas Bergersen
  Managing Director / Senior Geophysicist, Acoustic Imaging. Shallow water speciality. Major impact on analysis, visualisation, interpretation of seafloor, sub-bottom, and water column data in Australia over 25 years.
Paul Johnson
  Co-Director of AI-MAC. Principal Investigator of the Multibeam Advisory Committee (MAC) US since its inception in 2011. Data Manager UNH COM.
Kevin Jerram
  Investigator MAC Group. Acoustic Engineer. Specality in fisheries systems. UNH CCOM Ocean Engineering.

## Slide 5: Service Approach
Risk minimisation for survey client:
  Objective assessment and accessible performance metrics of any proposed survey system to ensure suitability for industry requirements.
Risk minimisation for survey provider:
  Objective decision making prior to commencement of survey for knowing whether proposed solution will be able to deliver final product. Know Before You Go.
Environment
Vessel
Hardware
Software
Human Factors
AI-MAC
Notes: Service beneficial to all.
Risk mitigation for the survey client or stakeholder through OJECTIVE ASSESSMENT and accessible performance metrics of a proposed system…..THIS IS WHERE THIS GRIUP COMES INTO IT ….it should be a repository kept within a group like this. And functionality.
PUBLISHED and help in a repository.
RISk mitigation for the survey contractor – prior to survey know what to expect.
FROM EVNRIONEMT, as applied to vessel, with particular set of hardware, software and acknowledging human bias/human factor of those on boar.d
(1) stakeholder (survey tenderer) for assessment of proposed solutions or
by contract (tender respondent) for confidence (risk reduction) that their proposed solution will deliver the required product or
commercial, defence, government organisation looking to procure new equipment for a particular vessel in a particular environment or

## Slide 6: Service Components
Desktop Study (sonar acoustic equations, use case, environment)
Node Survey (measure systematic bias)
Installation
Calibration / Validation (remove systematic and human bias)
Baseline Performance and Functionality Testing (use cases, environment)
Evaluation / Reporting / Upload to Repository
Annual Performance Check (Preventative maintenance)
Desktop
Node Survey
Installation
Cal/Val
BPF Test
Eval/Report
Annual Check
TRAINING
Notes: Desk top study = proposed use cases relative to sonar equations in environment of operation.
Should consist of : survey type and data types required, desired survey speed, rate of progress, range of survey depths, survey resolution per depth.
AI MAC service can be employed by:
Based around sonar equations, installation parameters (moon pool size / shape restrictions), water temp, depth, salinity, rate of progress for opportunistic data collection.
Node Survey for understanding relationship of all sensor sensing centres relative to each other (systems are integrated).
Installation – based on best practice and understanding of methodology / data volume computations and data handling and management.
Calibration / validation – data derivation of system as installation for 1. rigidity and 2 data derived= measured. Removal of all systematic bias regardless of the orgin of it (could be human error : user input error, node survey error, non-rigid platofmr).
BPT – baselining system as installed (system + vessel ambient acoustics across range of user cases within operation al parameters).
INCLUDES: SELF NOISE TESTING (vessel noise contribution to MBES)
Bublle sweep down assessmet – bubbles sweeping down hull and over array faces
Accuracy testing
Swath performance (v depth v speed v frequency) extinction v speed, depth & frequency
Backscatter validation
Water column validation
Acoustic interference and vessel self-noise testing v speed and heading – changes in shi[
Eval / Report – snap shot of BPT
Shakedown – tracking of performance, configuration, feeds into maintenance.

## Slide 7: Benefits of Service
Know Before you Go
  System performance and functionality is established, reported on and uploaded to a national repository across a variety of survey environments and objectives.
Unbiased Assessment of Performance
  Independent of direct manufacturer participation during trials
Optimisation of Equipment Running Costs
  Record of system performance (repository) makes identification of degrading performance easier and less subjective
  Preventative maintenance can be more efficiently scheduled into survey programs
Notes: Repository – upload to repository

## Slide 8: Benefits of Service
Better data
  Metrics proving system capabilities for a range of use and environment cases
  Indisputable proof of correctness and known uncertainty
  Long term survey programs (e.g., monitoring objectives) will produce more valid results
  Data logged in such a manner that independent assessment of quality can be conducted, and hence to what degree should data set contribute to a national MBES database (bathymetry/backscatter/water column)
  Higher likelihood that post-processing remediation efforts can correct errors made during data acquisition.

## Slide 9: Case Study : E/V Nautlius
Mapping on US West Coast May-Oct 2017
  Kongsberg EM302 multibeam sonar
  Different voyage leader per campaign
Baseline Performance Report and Annual Shakedown from MAC group
  Most recently Spring (April) 2017
Reduced performance noted during Sept 2017 survey (qualitative indicators, reduced swath, increased noise in water column, etc.)
Performance compared with baseline expectations from Spring 2017 report.
Fast (and objective) isolation of issue (contrary to human bias)
Remediation single day, assess performance.
Notes: Can we show bad extincition v good extinction here.
Talk through steps that L Gee applied to
Identify noise
Consult baseline report + most recent shakedown
Note degradation
Isolate following report
Address by deciding and direction vessel to port
Addressing
Testing

## Slide 10: Extinction Plots
Depth (metres) v swath width (metres)
Notes: NA080 plot late May after pump change at 3,000m had average 6500m swath was good but didn’t conduct full tests
NA088 in mid-September was down to about 5000m and already reducing with depth
NA089 after clean was back over 7k and getting over 8k swath in 4,000m depth
Base line performance metrics, yes, issue tests to isolate, did that made remediation in port quicker and easier
Base line – Spring 2017 as performance tested for area and documented. 6,500 metres swath but full tests not carried out (only to depth of 3.5km)
What they saw – in Sept 2017 – swath width 5km – referred to baline performance test, identify issue, isolate reasons, decision to go to port
After cleaning over 8km swath in 4000m water.

## Slide 11: Tx fouling April to September - worse than expected
Notes: Why this bad – good question!
Contributing factors:
found out later that divers cleaned transducers in early March not May, and first cruise late April.
Nautilus on DP for significant periods for ROV diving June to September
Saw significant upwelling in some areas on the west coast this year (e.g. Olympic Coast) that potentially contribute to quicker growth than expected
So documents pointed to every reason why there should not have been excessive fouling on the MBES tranducer. But in realty it hadn’t been completed, coupled with West Coast upwelling during summer.
Moral – DATA TELLS the story ….baseline report provides the system baselines and functionality …..isolatation fast, addressing issue and remediation fast.

## Slide 12: Case Study : RV Solander
AIMS Research Vessel outfitted with new systems and sensors using the AI-MAC approach 2017.
Timeline June-Sept 2017:
  Desktop nalysis of Use cases and operational parameters
  Selection by AIMS of systems based on capability matrix
  Installation and integration
  Calibration and Validation
  Baseline Performance Testing and Functionality Analysis
Training ongoing - getting users comfortable in system use, troubleshooting problems during acquisition through isolation and reference to baseline, processing and products at the back end.
Annual Performance Review already in the schedule
Notes: Check not only performance but also functionality MENTION ANALYSIS TYPES :
BASELINE PERFORMANCE TESTING LIST OUT TESTS:
Bubble Sweep Down – tendency of bubbles

## Slide 13: Summary and Recommendations
Rigorous process that should be a part of National Survey Guidelines and any program with expectations of contributing to a national MBES database.
Independent of hardware and software manufacturers.
Tailored to examine both functionality and baseline performance of any system.
Proven techniques employed locally and internationally Australian-developed service available now in Australia.
Standardised Reporting of Performance Baselines and Functionality should be part of a national MBES database.

## Slide 14
Questions?
2016
2017